# SCSI2SD Quick Start Guide
## Configuration
Configuration settings are stored on the SD card. The settings can be managed by the scsi2sd-util6 program, which connects to the board over USB. The SD card must be inserted into the SCSI2SD board for this to work.
Note that in previous SCSI2SD hardware versions the configuration was stored internally to the device and not on the SD card.
Please download a copy of scsi2sd-util6 from http://www.codesrc.com/files/scsi2sd-v6/latest
The default options are very conservative to ensure the device works with most older SCSI hosts “out of the box”. You may wish to enable some of the performance options if you’re using the board with a SCSI2 system instead of an older SASI/SCSI1 system.
Option	Default value
SCSI ID	0
Virtual disk size	2GB
Terminator	Enabled

## Connecting to your system
### Termination
Both ends of the SCSI chain must be terminated. Insufficient termination, or excess termination, will cause the SCSI chain to misbehave or not work at all.
If the SCSI2SD is the only SCSI device, then termination must be enabled (default)
### Power
The SCSI2SD may be powered by either the SCSI cable (ie. self-powered), floppy connector, or USB cable.
- Some systems do NOT provide power over the SCSI cable, including many musical samplers.
- The SCSI2SD is a 5V device. Do not swap 5V and 12V wires if making a DIY floppy power cable. It’s best to simply never connect the 12V wire.
## Firmware Updates
Updates are performed over USB using the standard Device Firmware Upgrade device class. scsi2sd-util6 provides a simple interface to dfu-util (http://dfu-util.sourceforge.net) for updating the firmware.
## Microsoft Windows
The dfu-util.exe program must be in the same location as scsi2sd-util6.exe. A copy may be downloaded from the same place as scsi2sd-util6.
A driver is required for firmware updates. Please download and install from http://www.codesrc.com/files/scsi2sd-v6/latest/windows/driver.
## Apple OSX
The dfu-util.exe program may be either in the same location as scsi2sd-util6.exe, on available on the $PATH. A copy is included in the scsi2sd-util .dmg file.
## Linux
Please install your distributions dfu-util package.
eg. Debian/Ubuntu: sudo aptitude install dfu-util
### Failsafe Firmware Updates
A failsafe update is only necessary if a normal update attempt fails unexpectedly (eg. the cable was removed before it was complete), or if bad development firmware was loaded onto the board. To force a firmware update the SCSI2SD needs to be reset into the bootloader mode.
1. Place a shunt over the jumper labelled “BOOTLDR”
2. Reset the device (ie. remove all sources of power then reconnect the USB cable).
3. Update firmware as usual.
## Bug Reports
Please report all issues to michael@codesrc.com. Please state the brand and model/size of SD card being used, as well as the SCSI host system (eg. “Apple Mac OS 7.5.3” or “Akai S3200”).