# SCSI2SD Quick Start Guide
## Warning
The SCSI2SD is a 5V device. Do not swap 5V and 12V wires if making a DIY floppy power cable. It’s best to simply never connect the 12V wire.
Do not install the board directly on metal, as this will short the contacts on the scsi2sd.
## Configuration
Configuration settings are stored on the SD card. The settings can be managed by the scsi2sd-util6 program, which connects to the board over USB. The SD card must be inserted into the SCSI2SD board for this to work.
Please download a copy of scsi2sd-util6 from http://www.codesrc.com/files/scsi2sd-v6/latest
The default options are very conservative to ensure the device works with most older SCSI hosts “out of the box”.
Option	Default value
SCSI ID	0
Virtual disk size	2GB / Some older samplers fail with disks larger or equal to 1GB.
Terminator	Enabled
Selection Delay	255 (auto) / Some older hosts require manually setting 0 or 1.
Parity	Disabled / It’s a good idea to enable this option if supported by your system to prevent data corruption.
SCSI2 Mode	Disabled / The SCSI2 mode requires all cabling to meet the SCSI2 standards. Ensure SCSI2 is disabled when using Centronics and DB25 cables

## Termination
Both ends of the SCSI chain must be terminated. Insufficient termination, or excess termination, will cause the SCSI chain to misbehave or not work at all.
- If the SCSI2SD is the only SCSI device, then termination must be enabled (default).
- Active terminators must be used if SCSI2 mode is enabled. The SCSI2SD board has an integrated active terminator.
## Power
The SCSI2SD may be powered by either the SCSI cable (ie. self-powered), floppy connector, or USB cable.
Some systems do NOT provide power over the SCSI cable, including many musical samplers.
A good ground connection to the SCSI controller is essential. An additional ground wire may be required if:
1. Power is provided over the SCSI cable or USB, or from a different power supply to the SCSI controller (eg. external drive box), and
2. Long SCSI cables, cable adapters, or multiple devices are present.
A ground wire may be connected from the floppy power connector (inner 2 pins) to the chassis of the computer.
## Firmware Updates
Updates are performed over USB using the standard Device Firmware Upgrade device class. scsi2sd-util6 provides a simple interface to dfu-util (http://dfu-util.sourceforge.net) for updating the firmware.
## Microsoft Windows
The dfu-util.exe program must be in the same location as scsi2sd-util6.exe. A copy may be downloaded from the same place as scsi2sd-util6.
A driver is required for firmware updates. Please download and install from http://www.codesrc.com/files/scsi2sd-v6/latest/windows/driver.
* For those who have used the STM DfuSe software previously, the existing driver for the “STM32 BOOTLOADER” device must be uninstalled. http://zadig.akeo.ie/ can simplify the uninstallation of the old driver, and installation of the WinUSB driver.
## Apple OSX
The dfu-util.exe program may be either in the same location as scsi2sd-util6.exe, on available on the $PATH. A copy is included in the scsi2sd-util .dmg file.
## Linux
Please install your distributions dfu-util package.
eg. Debian/Ubuntu: sudo aptitude install dfu-util
### Failsafe Firmware Updates
A failsafe update is only necessary if a normal update attempt fails unexpectedly (eg. the cable was removed before it was complete), or if bad development firmware was loaded onto the board. To force a firmware update the SCSI2SD needs to be reset into the bootloader mode.
1. Place a shunt over the jumper labelled “BOOTLDR”
2. Reset the device (ie. remove all sources of power then reconnect the USB cable).
3. Update firmware as usual.
## Bug Reports
Please report all issues to michael@codesrc.com. Please state the brand and model/size of SD card being used, as well as the SCSI host system (eg. “Apple Mac OS 7.5.3” or “Akai S3200”).