# SCSI2SD Quick Start Guide

## Configuration
Configuration settings are stored on the SD card. The settings can be managed by the scsi2sd-util6 program, which connects to the board over USB. The SD card must be inserted into the SCSI2SD board for this to work.
Note that in previous SCSI2SD hardware versions the configuration was stored internally to the device and not on the SD card.
Please download a copy of scsi2sd-util6 from http://www.codesrc.com/files/scsi2sd-v6/latest
The default options are very conservative to ensure the device works with most older SCSI hosts “out of the box”. You may wish to enable some of the performance options if you’re using the board with a SCSI2 system instead of an older SASI/SCSI1 system.
Option	Default value
SCSI ID	0
Virtual disk size	2GB
Terminator	Enabled

## Connecting to your system
Termination
Power

## Firmware Updates

Done over USB using the Device Firmware Upgrade device class.
May use standard dfu utilities. I’ve tested:
- dfu-util (http://dfu-util.sourceforge.net/)
- STMicroelectronics DfuSe software (http://www.st.com/content/st_com/en/products/development-tools/software-development-tools/stm32-software-development-tools/stm32-programmers/stsw-stm32080.html)
To upgrade the firmware the SCSI2SD needs to be reset into the bootloader mode. The scsi2sd-util6 software will attempt to do this automatically. If this fails, you may force the SCSI2SD to enter the bootloader mode:
1. Place a shunt over the jumper labelled “BOOTLDR”
2. Reset the device (ie. remove all sources of power then reconnect the USB cable).
### BETA Limitations
Firmware updates via scsi2sd-util6 are not fully functional. It attempts to run the dfu-util program, which is not supplied. Linux users may install dfu-util if available via their OS distribution and use scsi2sd-util6, Windows users should run the STMicroelectronics DfuSe software, and Mac users should wait until scsi2sd-util6 is updated to ship with dfu-util.